## Slide 1
INFECTION PREVENTION AND CONTROL DECONTAMINATION
.

## Slide 2: Learning objectives
To describe the decontamination levels
To list the properties of an ideal chemical disinfectant.
To understand the factors that affect disinfection.
To understand the Jik preparation procedure
To describe how to decontaminate different surfaces.

## Slide 3: What is Decontamination?
Decontamination renders an item safe for handling and reuse
Cleaning, Disinfection and Sterilization, are ALL examples of Decontamination

## Slide 4: What are the 3 Decontamination Levels?
Cleaning is the removal of soil, debris and organic matter to render the item aesthetically acceptable
Disinfection is the removal of all pathogens. A few spores may remain.
Sterilization is the removal of all organisms, including spores

## Slide 5: Risks During Cleaning and Disinfection
Poor cleaning & disinfection can spread infection to:
  Patients
  Cleaners
  Visitors
  Staff
Cleaners should always:
  Wear appropriate PPE
  Follow procedures exactly

## Slide 6: Why must we clean before disinfection?
Answer:
Organic matter (e.g., body fluids):
  Neutralizes chlorine (stops it killing organisms)
  Prevents chlorine from getting to the organisms

## Slide 7: Why do we need remove chlorine residue?
Answer:
It corrodes and damages bare metal
It reduces life of plastic and cotton
Cannot be left on medical instruments - it is toxic to skin and mucous membranes
It leaves a white deposit on floors

## Slide 8: DISINFECTION
This can be achieved with heat or chemicals.
Disinfectants must be
  Used for the right purpose,
  In the appropriate concentration,
  For the prescribed length of time,
  Following the manufacturer's instructions.
  Be kept in their stock concentration,
  Used when freshly diluted

## Slide 9: Disinfectant use (1)
While using disinfectants and antiseptics, it is vital that manufactures’’ instruction are followed for maximum effectiveness.
Always measure and never guess the amount of water and disinfectant to be mixed. Too high a concentration is wasteful and hazardous while too low a concentration is ineffective.
Do not mix antiseptics or disinfectants as this reduces their effectiveness due to chemical interaction.

## Slide 10: Disinfectant use (2)
Observe the minimum contact time for each disinfectant used.
Disinfectants are not recommended for damp dusting unless there is spillage of blood or body secretions.
Use freshly prepared disinfectants.

## Slide 11: Choice of disinfectant(1)
The choice of disinfectant will depend on the following:
1. Patient susceptibility to infection
Immuno-compromised patients will need high level disinfection or sterilization for the
devices used on them.
2. Tolerance of device to heat, chemical, pressure, moisture.
Devices such as endoscopes and other fiber-optic equipment cannot withstand temperatures required to achieve high-level disinfection and therefore chemical are used.
3. Nature of contamination/micro-organisms suspected.
More resistant organisms and spore forming organisms will require sterilization instead of chemical disinfection.

## Slide 12: Choice of disinfectant cont’d
4. Time available for processing
  Chemical disinfection is quicker than heat method although heat is the preferred option.
  When choosing a chemical method, it should be effective (see table on choices
  of disinfectant).
5. Risks to processing staff
  Some chemicals are highly toxic and can adversely affect the staff using them.
6. Cost of processing
7. Availability of processing equipment

## Slide 13: Properties of ideal Chemical Disinfectant
Broad spectrum: | should have a wide antimicrobial spectrum
Fast acting: | should produce a rapid kill
Not affected by environmental factors: | should be active in the presence of organic matter (e.g., blood, sputum, feces) and compatible with soaps, detergents, and other chemicals encountered in use

## Slide 14: Properties of ideal Chemical Disinfectant
Nontoxic: | should not be harmful to the user or patient
Surface compatibility: | should not corrode instruments and metallic surfaces and should not cause the deterioration of cloth, rubber, plastics, and other materials
Residual effect on treated surfaces: | should leave an antimicrobial film on the treated surface Easy to use with clear label directions
Odorless: | should have a pleasant odor or no odor to facilitate its routine use

## Slide 15: Properties of ideal Chemical Disinfectant
Economical: | should not be prohibitively high in cost
Solubility: | should be soluble in water
Stability: | should be stable in concentrate and use-dilution
Cleaner: | should have good cleaning properties
Environmentally friendly: | should not damage the environment on disposal

## Slide 16: Factors affecting Disinfection
Environmental Factors
Dried spills (from media, buffers) may limit contact between the disinfectant and the target organism.
  Pre-cleaning usually necessary for spills
Dirt, grease and oils - all can protect the organisms.
  Grease and oils will repel water based disinfectants.

## Slide 17: Factors affecting disinfection
Product Factors
Age of the product/solution
Method of application
  spray vs. wipe
Rate of application
Storage conditions
  Opaque vs. clear containers

## Slide 18
Resistance to disinfectants
Number of microorganisms
Location of microorganisms
Innate resistance to the disinfectant
Concentration and potency of the disinfectant
Physical and chemical factors
Presence of organic matter
Duration of exposure
Biofilms
Note: resistance decreases in the descending order of the above list
Susceptibility
Resistant
Factors affecting Disinfection

## Slide 19: Factors affecting Disinfection
Resistance of micro-organisms
Some micro-organisms are more resistant to disinfection than others.
The generally accepted order from the most resistant to the least resistant is: bacterial spores, Mycobacterium, hydrophilic viruses, fungi, vegetative bacteria, lipid viruses.
For example: a spill with a small concentration of bacterial spores will require longer disinfection time than a large concentration of lipid viruses.

## Slide 20: Factors affecting Disinfection
Type and concentration of disinfectant used
Resistance of micro-organisms depends on the type of disinfectant used. A particular micro-organism may be more resistant to one type of disinfectant than another. For instance, alcohol (isopropyl or ethyl) is effective against vegetative bacteria and most lipophilic viruses, but is not effective against bacterial spores or most hydrophilic viruses.
Many disinfectants are broad spectrum; that is, effective against all or most forms of microbial life.

## Slide 21: Disinfectants Uses, Advantages, and Disadvantages
Disinfecting agents | Spectrum (level) | Uses | Advantages | Disadvantages
Alcohols (60-90%) Including ethanol, isopropanol | Low to intermediate | Semi-critical and on-critical · Thermometers, stethoscopes · Rubber stoppers on multi-dose vials · Spot cleaning on surfaces | Fast acting · No residue · No staining · Low cost · Widely available | Volatile flammable · Irritant to mucous membranes · Inactivated by organic matter · May harden rubber, cause glue detoriation or crack acrylic
Chlorine & related Compounds Sodium hypochlorite (5.25% -6.15%) house bleach at a concentration of 100-5000 ppm free chlorine | Low to high | Tonometers Spot disinfection of surfaces Dental appliances Hydrotherapy tanks Water system in haemodialysis (high concentration or chlorine gas. | Low cost Fast acting Readily available Liquid, tablets, powder | Corrosive to metal in high concentrations (>500 ppm) · Inactivated by organic matter · Discolouration / bleaching of fabrics · Releases toxic chlorine gas when mixed with ammonia. · Skin and mucous membrane irritant· Unstable if left uncovered, exposed to light or diluted

## Slide 22: Disinfectants Uses, Advantages, and Disadvantages cont’d
Disinfecting agents | Spectrum (level) | Uses | Advantages | Disadvantages
Aldehydes Glutaraldehyde > 2% aqueous solution buffered to pH 7, 5-8, 5 with sodium bicarbonate | High level to sterilant | Endoscopes (20 min at 20 C) | Good material compatibility | Allergenic, irritant to skin and respiratory tract. · Direct contact causes skin injury · Relatively slow activity against M. tuberculosis
Peracetic acid 0.2 –0.35% and other stabilised organic acids | High level to sterilant | Automated endoscopic systems · Sterilisation of heat sensitive items e.g. haemodialysers · Suitable for manual instrument processing | Rapid sterilization cycle time at low temperature (20-45 min at 50-550C) · Active in the presence of organic matter ·Environmentally friendly by products (water,oxygen, acetic acid) | Corrosive to some metals · Unstable when activated · May irritate skin, conjunctivae, mucous membranes

## Slide 23: Disinfectants Uses, Advantages, and Disadvantages cont’d
Disinfecting agents | Spectrum (level) | Uses | Advantages | Disadvantages
Orthoflphthalal-dehyde, 0.55% | High level to sterilant | Endoscopes | . Excellent stability over wide pH range · No need for activation · Superior mycobactericidal activity compared with glutaraldehyde | . More expensive · Stains skin and mucous membranes · Stains items not thoroughly cleaned · Eye irritation on contact · Hypersensitivity reactions · Slow sporocidal activity · Monitoring for continuing efficacy levels
Hydrogen peroxide 7.5% | High level to sterilant | . Cold sterilization for heat-sensitive items · 30 min at 20 C. | . No activation · No odour · Ecofriendly | Material compatibility concerns with metals such as brass, copper zinc etc.

## Slide 24: Disinfectants Uses, Advantages, and Disadvantages cont’d
Disinfecting agents | Spectrum (level) | Uses | Advantages | Disadvantages
Hydrogen peroxide 7.5% plus peracetic acid 0.23% | High level to sterilant | Haemodialysis disinfection | . Fast acting (high level disinfection in 15 min) · No odour · No activation required | . Materials compatibility concerns with metals such as brass,copper, zinc etc · Damage to eye skin
Glucoprotamin | High level | Manual endoscope processing 15 min at 20 C | . Good mycobactericidal activity · High cleansing performance · No odour | Lack of activity against some spores and enteroviruses

## Slide 25: Disinfectants Uses, Advantages, and Disadvantages cont’d
Disinfecting agents | Spectrum (level) | Uses | Advantages | Disadvantages
Phenolics | Low to intermediate | Environmental decontamination and non-critical items. To be avoided | . Not inactivated by organic matter | Leaves a residual film on surfaces · Harmful to the environment · No antiviral activity · Reported hyperbilirubinaemia in infants (avoid in nurseries)
Iodophores (30-50 ppm free chlorine) | Low level | . Disinfection of non-critical items, hydrotherapy tanks · Main use is as anantiseptic (2-3 ppm chlorine) | . Relatively nonirritating and nontoxic | . Inactivated by organic matter · Adverse reaction with silicone tubing · May stain fabric · Not commonly in use as a disinfectant.

## Slide 26: Materials for Cleaning & Disinfection
Appropriate PPE
Soap and water
Absorbent material (cloths, paper towel)
Bucket, mop, cloths
Chlorine solution (0.5% Solution)
General waste bin
Medical waste bin

## Slide 27: Preparation of jik

## Slide 28: Preparation of jik

## Slide 29: Clean General Nursing Care Surfaces(Floors, walls, tables etc)
Use disposable towels or a mop soaked with soapy water to wipe surfaces
Ensure all visible dirt/debris is removed
Pay particular attention to high-touch surfaces
e.g. light switches, beds, mobile equipment.
Dry surface to ensure non-slip (or place signage)
Dispose these towels into general waste bin

## Slide 30: Disinfection of Isolation Unit Surfaces
Wear appropriate PPE
Clean as for General Wards
Disinfect by wiping all surfaces with disposable towels or mop soaked with strong (0.5%) chlorine
Allow Chlorine to act for 10 mins.
Wipe surface with water-dampened cloth
Dispose of towels in medical waste bin
Wash mops, disinfect in 0.5% chlorine
for 10 mins, air dry (preferably in sun).

## Slide 31: Disinfection of Spills in Isolation Unit Surfaces
Wear appropriate PPE
Using absorbent material, (cloth, paper etc), wipe up all visible excreta.
Dispose of materials into medical waste bin
Clean and disinfect surface as per Isolation Unit procedure
WHO Practical Guidelines for Infection Control in Health Care Facilities 2004
http://www.wpro.who.int/publications/docs/practical_guidelines_infection_control.pdf.

## Slide 32: Important Points to Remember for Spills
Do not pour solutions directly on spilled body fluids (can create splashes or spread the spill)
Instead, pour solutions (such as strong 0.5% chlorine solution) onto towels and then use these moist towels for disinfecting
Notes: Do not use mops for spills of body fluids until:
  Visible debris has been removed, and
  Surface has been disinfected after removal of contamination

## Slide 33: Recommended Cleaning & Disinfection Frequencies
Item | Frequency
Surfaces in screening area | At least twice daily After a suspect Ebola patient is screened
Surfaces in general nursing care area | At least once daily When visibly soiled
Linens and mattresses | After every patient When visibly soiled
Latrines/toilets | At least twice daily When visibly soiled
Isolation area | At least twice daily while occupied After any spill, and after a patient leaves

## Slide 34: Decontaminating medical devices
Level
Contact with
Decontamination
Process
e.g.
Sterile tissue
e.g. Implant
Sterilization
Autoclave
-
-
Mucous
memb
Non
intact skin
e.g. speculum
High
level
disinfection
Boiling
Critical
Semi
critical
Non
critical
level
Intact skin
e.g. stethoscope
Low
-
disinfection
70%
Alcohol

## Slide 35: Alternative High Level Disinfection of Medical Equipment
Clean with soap and water first
Soak in 0.5% chlorine for 10 minutes
Rinse with clean water
Dry with clean towel

## Slide 36: How to Manage Contaminated Linen
Linen soiled with blood/excreta:
Use gown & gloves when handling
Scrape off blood/excreta carefully into bucket using tongue depressor.
Place linens into leak-proof bags or buckets labeled “soiled” for transport to laundry
If washing by hand wear heavy-duty gloves, gown, face-shield and mask.

## Slide 37: Item/object and recommended Method or Procedure for Disinfection/ Decontamination
Item | Method/Procedure | Remarks
Respiratory Equipment; multiple use circuits | Heat disinfect for 20 minutes or 0.5-1% hypochlorite for 20 minutes, wash thoroughly and dry | Some may be autoclaved Check manufacturers’ guidelines. Use of filters is recommended
Humidifiers | It is heat disinfected after each patient and when respiratory circuit is changed | Empty daily and refill with sterile water
. Ambu-bags · Neonatal respirators · Incubators · Resuscitators | Heat disinfection or use of 2% gluteraldehyde | Rinse thoroughly with sterile water after gluteraldehyde
Suction catheters · Oxygen tubes | Are disposable, never share between patients Rinse with sterile water when in use Staff must disinfect their hands before and after use with alcohol | 

## Slide 38: Item/object and recommended Method or Procedure for Disinfection/ Decontamination cont’d
Item | Method/Procedure | Remarks
Mucous membranes | 0.1% Chlorohexidine | 
Clean wounds | 0.05 Chlorohexidine | 
Contaminated Wounds | Irrigate with Povidone Iodine or Chlorohexidine with cetrimide | 
Necrotic Wounds | Hydrogen Peroxide | Follow Instructions
Burns | Clean with sterile saline and apply sufratulle | Observe high level of hygiene especially hand hygiene
Environment: Smooth hard clean surface e.g. trolley tops, laboratory benches and Desks | Wipe with 70% Ethyl or Isopropyl alcohol | These surfaces must be clean and dry before disinfection

## Slide 39: Item/object and recommended Method or Procedure for Disinfection/ Decontamination cont’d
Item | Method/Procedure | Remarks
When hazard of viral infection is present in general ward, e.g. sinks, wash-basins, drainages and baths | Disinfect with 1% hypochlorite, then scrub with Scouring powder (VIM) | 
Skin preparation before invasive procedures | Use Povidone Iodine or · 70% ethyl or isopropyl alcohol Or · 0.5% Chlorohexidine gluconate in 70% alcohol | The alcohol disinfectants should be avoided if the diathermy machine is going to be used, to avoid sparking off a fire
Oxygen delivery masks | Wash thoroughly, dry and wipe with 70% Isopropyl alcohol | 
Neonatal and pediatric Unit incubators | Wash with soap and water, dry and wipe with isopropyl alcohol all surfaces daily | · To avoid cross infection · Terminal cleaning after patient is discharge or dead

## Slide 40: Item/object and recommended Method or Procedure for Disinfection/ Decontamination cont’d
Item | Method/Procedure | Remarks
Humidifiers for Neonates | · Autoclave or boil for 20 minutes | · To avoid cross infection
Resuscitators | · Disconnect the different parts · Wash and autoclave | 
Fibro scopes e.g. Endoscopes Laparoscopes Custoscopes Bronchoscopes | · They are heat sensitive · Wash with detergent and water · Use 2% gluteraldehyde for 20 minutes then rinse with distilled water | · If you suspect TB, 2% gluteraldehyde for 3 hours · Emphasis should be put on pre-cleaning · Ensure correct type of glutaraldehyde to avoid damage
Proctoscopes and Sigmoidoscopes | Cleaned, sterilized or disinfected with 2% gluteraldehyde then rinse with sterile water | 

## Slide 41: Item/object and recommended Method or Procedure for Disinfection/ Decontamination cont’d
Item | Method/Procedure | Remarks
Non heat sensitive equipment,e.g. bedpans, urinals, kidney dishes, heavy duty rubber tubes, floor mops, brushes for scrubbing, soiled linen, cheatle forceps, and bowls | · Wash thoroughly with soap and water, rinse an boil for 20 minutes. If contaminated with blood or other body fluids, first disinfect with hypochlorite, then wash and boil | · Decontamination before washing protects staffs who handle/clean these items
General environment (clean surface) · Body fluids spillage or heavy soiling | · 0.1 – 0.5% hypochlorite (1000 – 5000 PPM) chlorine · 0.5% - 1% hypochlorite(5,000 –10,000), then wash with soap and water | · May be applicable for delivery beds and theatre operating table · Powder or granules may be used
Terminal cleaning of rooms after outbreaks, e.g. · Tetanus, Cholera, Small Pox, Gas Gangrene,Ebola,Plague | · 8% Formaldehyde fumigation · Clean thoroughly before re-use of facility | · Place should be closed for 3 days Where space for new patients is a problem, fumigate, and close facility for 24 hours. Clean thoroughly with soap and water and re-occupy
Disinfection by ultra violet rays can be used in the laboratory, theatre, and mortuary. It clear most of the vegetative organisms but not spores |  | 

## Slide 42: Methods of decontaminating routinely used items
Item or site | Preferred method | Alternative methods / comments
Airways and Endo tracheal tubes | · Single-use disposal or · Head sterilized in SSD | · Use disposable for airborne diseases if heat sterilization not available.
Ambu bags | · Send to SSD for heat disinfection | · Ethylene oxide
Ampoules | · Wipe with 70% isopropyl alcohol and allow to dry before opening. | · Do not immerse in disinfectant
Bath water | · No addition of antiseptic routinely unless burns patient. | · Antiseptics increase GNB colonization
Baths | · Clean with detergent and nonabrasive cream cleanser, Rinse and dry. | · Infected patients. As previous column. Wipe over with chlorine-based agent. Do not soak.
Bed and cots | · Wipe with warm water and detergent to remove all visible signs of dust and dirty. Dry. | · Disinfectant unnecessary

## Slide 43: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Bed frames | · Wipe with warm water and detergent. Dry. | 
Bed locker | · Wipe with warm water and detergent. Dry. · Clean inside locker once patient has been discharged | 
Bedpans and urinals | · Wear non-sterile gloves · Empty contents directly into ward washer disinfector (80% 0C x 1min). Inspect for cleanliness after removal. Clean if necessary and store inverted to dry | · Macerators with paper-mache bedpans and urinals. · Manual cleaning: Empty into sluice. Clean bedpans thoroughly with a scrubbing brush and detergent. Rinse. Invert to dry. · Never soak bedpans
Baths | · Clean with detergent and nonabrasive cream cleanser, Rinse and dry. | · Infected patients. As previous column. Wipe over with chlorine-based agent. Do not soak.
Bed and cots | · Wipe with warm water and detergent to remove all visible signs of dust and dirty. Dry. | · Disinfectant unnecessary

## Slide 44: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Blankets and bed covers | · Change after each patient has been discharged or when visibly soiled. Send to laundry to wash at 80C | · Do not allow bedding from home; these may be infected with bedbugs or carry scabies
Bowls(dressing, surgical) | · Return to SSD | · Disposable
Bowls (patient wash) | · Wash with detergent, rinse and store inverted to dry | · Modern ward washer –disinfectors can also wash bowls · Use fresh water and towels for each patient
Carpets | · Daily vacuum (vacuum cleaner fitted with a filter) · Shampoo periodically and extract | · Not recommended in clinical areas.
Commodes | Wash seat daily with detergent and hot water and dry with a disposable paper towel. · Wipe the commode seat with a large alcohol wipe after each use | · If visibly contaminated, remove soil with tissue. Wash with warm water and detergent. Dry. · Enteric diseases: Viral – wipe hypochlorite (1000 ppm avCl2); bacterial – use 2%phenolic.

## Slide 45: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Computer and keyboards | · Damp dust daily · Wipe keyboard carefully to remove visible dirt | · Use a keyboard cover which is changed frequently
Crockery and cutlery | · Wash at 800C in dishwasher. · Manual cleaning. Wear gloves and hand wash in detergent and hot water (600C). Rinse and dry. | · Wear domestic gloves for manual cleaning · Infected patients; Unless instructed by IPC team treat as routine. · Disposable crockery is rarely used - e.g. Rabies
Curtains | · Change curtains frequently · Isolation room curtains should be changed with each terminal clean | · Blinds; both vertical and horizontal are difficult to clean and wash regularly.
Drains | · Clean regularly | · Chemical disinfectants are not recommended

## Slide 46: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Dressing trolleys* | · Remove all items daily and wipe surface with warm water and detergent. Wipe over with 70% isopropyl alcohol. · Discard all previous contents of open jars and bottles. Replace with unopened containers | · If open jars are used, keep the volume small so that the containers can be heat disinfected when empty. Do not top up open disinfectant containers
Duvets | · Washable duvet cover, which allows good circulation of air, should be used and changed after each patient | · Dry-clean hands after each patient use
Endotracheal suction catheters | · Disposable – can be used for 24 hours on the same patient · Flush with sterile water after each use. Bowl is washed and dried after each suction and filled with sterile water only before use | Decontaminate hands thoroughly before carrying our suction · Do not share suction catheters between patients.
Feeding bottles (baby) | · Heat sterilized in SSD | · Wash thoroughly. Rinse and soak in a fresh hypochlorite solution (125 ppm available chlorine x 30 min). Remove, rinse and dry.

## Slide 47: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Floor cleaning · Dry, Wet | · Use dust-attracting mop · Use water and detergent only | · Sweeping not recommended · Disinfectants not recommended
Humidifiers | · Empty daily and heat disinfect after each patient use · Clean with warm water and detergent. Dry, Fill with sterile water only | · Not recommended. Use heat exchange filters.
Infant incubators | · Wash all removable parts and clean thoroughly with detergent. Dry with paper towel. | · Infected: After cleaning, wipe over with 70% isopropyl alcohol or hypochlorite (125 ppm ac CI2 ). Leave incubator to stand unused for 6 hours (aeration).
Instruments (surgical) | · To SSD | 
Kitchen cloths | · Daily: Wash in detergent and dry | · Disposal preferable

## Slide 48: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Lamps (examination) | · Wipe with detergent, rinse and dry. Wipe over with alcohol. | Disassemble before cleaning
Laryngoscopes | · Wash with detergent, rinse and dry. Wipe over with alcohol | Disassemble before cleaning
Linen (see section on Laundry) | · Automated methods | 
Mattresses | · Use water if impermeable cover. Clean with warm water and detergent. Dry thoroughly · Never admit patients to soiled, stained or damaged mattress. · If rubber covers are uncomfortable, cover with absorbable paper which is frequently changed | · Horse-hair and cotton filled mattresses are not recommended.
Mop bucket | · Daily: Wash in warm water and detergent and store inverted to dry | · Disinfectant unnecessary

## Slide 49: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Mops | · Daily: Detachable head sent to laundry for heat disinfection and dried. · Manual cleaning: Wear rubber gloves. Rinse thoroughly under running water. Wash in hot water and detergent until clean. Store inverted to dry | · Colour-coding of mops is useful to reduce cross contamination between clean and dirty areas and infectious isolation rooms · The sun can be used in warm countries.
Nail brushes | · Not recommended | · Single use and heat disinfection only
Nasogastric (feeding tubes) | · Disposable | · Cannot be recycled
Nebulisers | · Wash and dry the container and mask after each patient use. Store dry and protected from dust | · Head disinfection if necessary
Oxygen masks | · Disposable | · If re-useable, Wash thoroughly until visibly clean or use heat disinfection (SSD). Dry. Wipe with alcohol

## Slide 50: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods / comments
Patient toiletries | · Patients should bring their own soap, towels, shaving equipment and other personal items which should never be shared | 
Pillows (see mattresses) | · Use waterproof cover | 
Rectal thermometer | · Wash in detergent after each use. Wipe alcohol and store dry | 
Scissors | · Wipe over with 70% isopropyl alcohol before and after use | 
Scrubbing machine | · Drain reservoir after use. Wipe with a damp cloth and store dry. | 
Shaving brushes | · Not recommended | · Pre-operative skin shaving should only happen in the operating suite – never in the ward.

## Slide 51: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods /comments
Sheepskin | · Synthetic: Launder in machine · Natural: Hand wash in detergent and dry. | · Not recommended for routine use unless clinically indicated. Restrict to one patient use only.
Soap (hand washing) | · Tablet: Store dry. · Liquid: Wall-mounted dispenser. Single-use sachets or send for thorough cleaning after it is empty and refilled under aseptic conditions | · Tablet soaps are not recommended · Never top up – increases risk of GNB colonisation.
Shower head | · Should be removed and cleaned thoroughly each week· Soak in descaler if necessary | · Replace rubber washer with plastic ones to prevent legionnaires’ disease
Sputum container | · Disposable only | 
Suction machines | · Empty the reservoir in the sluice after use, wash with warm water and detergent and store dry. Send tubing to SSD for sterilisation or discard. Clean the surface and cover after each use | · PPE: non-sterile gloves and apron · Never leave fluid (secretions or disinfectant) in the reservoir if not in use

## Slide 52: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods /comments
Surfaces and ledges | · Damp dusting daily. Dry | 
Thermometer (oral) Electronic | · Wash and dry after each patient use. Wipe with 70% isopropyl alcohol and store dry. · Change sleeve after each use | · Never soak thermometers in disinfectants. · Never use without sleeve
Taps | · Elbow operated · Clean daily and keep dry | · Replace rubber with plastic washers to prevent legionnaires’ disease
Toilet seats | · Wash at least daily with detergent and dry | 
Tooth mugs | · Disposable or send to SDD between patients | 
Toys | · Soft: Machine wash, rinse and dry · Other: Wash with detergent, rinse and dry. Wipe with alcohol swab | · Do not share toys in an infected ward. Heavily soiled toys may have to be destroyed

## Slide 53: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods /comments
Tubing | · Disposable · Reprocessed in SSD | · Never use gluteraldehyde to disinfect respiratory equipment
Ultrasound | · Disinfect with 70% isopropyl alcohol between each patient use · Intra-vaginal: Cover probe with a condom for each patient. | 
Ventilators | · These are complex and should be cleaned and disinfected according to manufacturer’s instruction · Sometimes there are technicians in the facility who do the maintenance | · Remove tubing and send for heat disinfection to SSD (800C x 3 min) or chemical disinfection · Clean all inspiratory and expiratory connections · Change both sets of filters · Check efficiency of air movement · Reassemble · Clean the outside of ventilator · Register in logbook
Washbasins | · Clean with warm water and detergent, cream cleaner for stains · Disinfectants not recommended | 

## Slide 54: Methods of decontaminating routinely used items cont’d
Item or site | Preferred method | Alternative methods /comments
Wound suction (closed drainage) | · Remove lid and carefully remove inner liner containing fluid. Dispose of in either infectious waste container or sluice. · Wash and clean the outer cover, dry and replace bag. Check that the valves and connectors are clean and functioning. | · Send for heat disinfection after each patient use
X-ray-equipment | · Damp dust only | · Wipe with 70% isopropyl alcohol if disinfection required.

## Slide 56
Thank you